## Slide 1: Flow Chart for predict, classification and compare in new RICT
John Murray-Bligh
Based on meeting at FBA River Lab 26 Nov 2019
New Model 44 diagrams and notes modified in meeting at FBA River Lab 13 Nov 2018
Notes: John Murray-Bligh
+44 (0)7714 710 507
john@murray-bligh.fslife.co.uk
John.murray-bligh’environment-agency.gov.uk

## Slide 2
RICT prediction
Environmental data input
2. Calculate latitude longitude mean temperature & temperature range from NGR
WE1.4 (Section 6)
Original sources of data and algorithms
WFD72c Final Report
Relevant section in the new Functional Spec
1. Data validation
WE1.6 (Section 5)
warning and fail reports
3. Transform data
WE1.4(v) (Section 6.6)
4. Discriminant function score
DFScored
DFCOEFF_GB685.dat
DFCOEFF_NI.dat
WE1.3 (Section 7.5)
5. Mahalanobis distance
MahDistg
DFMEAN_GB685.dat
DFMEAN_NI.dat
WE1.3 (Section 7.6)
7. Environmental suitability
WE1.3, WE1.6(ii)
WE1.6(ii) (Section 7.8)
8. Prediction of index
ExpIDXi
IDXMean
WE1.5 (Section 7.9)
6. Probability of end group membership
Probg
WE1.3 (Section 7.7)
Prediction of taxa
ExpTAXAPRt,s
ExpTAXAABt,s
ExpTAXAPRABt,s,a
TAXAAB
TAXAPR
TAXAPRAB
WE1.5 (Section 7.10)
Classification

## Slide 3
RICT prediction Model 44
Input Environmental data
2. Calculate latitude longitude mean temperature & temperature range from NGR
WE1.4 (Section 6)
Original sources of data and algorithms
WFD72c Final Report
Relevant section in the new Functional Spec
From last tab on Ralph’s spreadsheet RICT (R and MS Azure) software - Independent code Testing Results v2.xls, worksheet Predictions_M44_GB
1. Data validation
WE1.6 (Section 5)
Validation limits needed for new variables
warning and fail reports
3. Transform data
WE1.4(v) (Section 6.6)
4. Discriminant function score
DFScored
New values on Ralph’s spreadsheet
WE1.3 (Section 7.5)
5. Mahalanobis distance
MahDistg
Ralph’s spreadsheet
WE1.3 (Section 7.6)
7. Environmental suitability
WE1.3, WE1.6(ii)
WE1.6(ii) (Section 7.8)
Ralph to calculate new suitability for new variables
8. Prediction of index
ExpIDXi
IDXMean
WE1.5 (Section 7.9)
6. Probability of end group membership
Probg
WE1.3 (Section 7.7)
Prediction of taxa
ExpTAXAPRt,s
ExpTAXAABt,s
ExpTAXAPRABt,s,a
TAXAAB
TAXAPR
TAXAPRAB
WE1.5 (Section 7.10)
Classification
If new site, check location and if necessary, alter grid reference
Extract EV data from database.
If system unable to provide data (near source or flat) derive EV data manually
Revision needed by John and Ralph or us
New data or code needed from Tim

## Slide 4: RICT classification Applying the conversion to the adjusted expected to give reference values
4. Convert adjusted expected to reference value
ExpIDXRef,i = ExpIDXadj,i / Ki
(Section 8.4)
2. Adjust expected
ExpIDXadj,i
Adjustment parameters WHPT Aj
Section WE 4.5
Section 4.6 (Table 6)
Ralph’s spreadsheet
(Section 8.2)
Sources of data and algorithms
WHPT and other Abundance-Weighted Indices A Report to the Scottish Environment Protection Agency.
WFD72c Final Report
Testing RICT predictions and classifications report
Relevant section in the new Functional Spec
From last tab on Ralph’s spreadsheet RICT (R and MS Azure) software - Independent code Testing Results v2.xls, worksheet Predictions_M44_GB
Blue boxes indicate a process step which is simulated
9. Bias corrected observed
ObsIDXirB = ObsIDXir + Ubiasir
Section 6.3.3
(Section 8.8)
3. EQR conversion factor
Ki
Section 5.5
(Section 8.3)
5. Simulated uncertainty in reference value ExpIDXRef,ir
= ExpIDXRef,i + eir
Section 6.4 (amended)
(Section 8.5)
8. Simulated variation in bias
Ubiasir
Section 6.3.3.3
(Section 8.9)
single season
spring and autumn season
13. MINTA
Section 1.7
(Section 8.13)
Compare
(optional)
10. EQR = Bias corrected observed ÷ reference value
EQRirB
= (ObsIDXirB ÷ ExpIDXRef,ir)
(Section 8.10)
11. Simulated two season average
EQRirB,SpAu
= (EQRirB,Sp + EQRirB,Au) / 2
(i.e. average of all seasons involved)
(Section 8.11)
12. Identify class using published EQR class (Monte-Carlo simulation)
Prob H
Prob G
Prob M
Prob P
Prob B
Most probable class
Section 6.5
(Section 8.12)
7. Simulated sampling variation in observed
ObsIDXir= ObsIDXi ZNormir * SDObsi
Section 6.3.2
(Section 8.7)
6. User input observed
ObsIDXi
User input observed sample bias UBiasis
Section 6.3.3
(Section 8.6)
1. Prediction
ExpIDXi
(Section 8.1)

## Slide 5: RICT classification – Model 44 Applying the conversion to the adjusted expected to give reference values
4. Convert adjusted expected to reference value
ExpIDXRef,i = ExpIDXadj,i / Ki
(Section 8.4)
2. Adjust expected
ExpIDXadj,i
Adjustment parameters WHPT Aj
Section WE 4.5
Section 4.6 (Table 6)
Ralph’s spreadsheet
(Section 8.2)
Sources of data and algorithms
WHPT and other Abundance-Weighted Indices A Report to the Scottish Environment Protection Agency.
WFD72c Final Report
Testing RICT predictions and classifications report
Relevant section in the new Functional Spec
From last tab on Ralph’s spreadsheet RICT (R and MS Azure) software - Independent code Testing Results v2.xls, worksheet Predictions_M44_GB
Blue boxes indicate a process step which is simulated
9. Bias corrected observed
ObsIDXirB = ObsIDXir + Ubiasir
Section 6.3.3
(Section 8.8)
3. EQR conversion factor
Ki
Section 5.5
(Section 8.3)
5. Simulated uncertainty in reference value ExpIDXRef,ir
= ExpIDXRef,i + eir
Section 6.4 (amended)
(Section 8.5)
Technically, this will differ from Model 1 because most EV data derived from GIS, but we don’t know its true error. Use same error values as Model 1 for safety
8. Simulated variation in bias
Ubiasir
Section 6.3.3.3
(Section 8.9)
single season
spring and autumn season
13. MINTA
Section 1.7
(Section 8.13)
Compare
(optional)
10. EQR = Bias corrected observed ÷ reference value
EQRirB
= (ObsIDXirB ÷ ExpIDXRef,ir)
(Section 8.10)
11. Simulated two season average
EQRirB,SpAu
= (EQRirB,Sp + EQRirB,Au) / 2
(i.e. average of all seasons involved)
(Section 8.11)
12. Identify class using published EQR class (Monte-Carlo simulation)
Prob H
Prob G
Prob M
Prob P
Prob B
Most probable class
Section 6.5
(Section 8.12)
7. Simulated sampling variation in observed
ObsIDXir= ObsIDXi ZNormir * SDObsi
Section 6.3.2
(Section 8.7)
6. User input observed
ObsIDXi
User input observed sample bias UBiasis
Section 6.3.3
(Section 8.6)
1. Prediction
ExpIDXi
(Section 8.1)

## Slide 6
RICT compare
Sources of data and algorithms
WFD72c Final Report, section 1.7 Procedure COMPARE: page 58
Information type:
Algorithms
Data
Classification
Site A
Classification
Site B
Difference
EQRB – EQRA =
DiffEQRirB
1.7
Confidence of change of class
Pdiff = 2 * minimum of (Pdiff0, PDiff1)
1.7
Estimated probability of change in status from class i to class j
PrChij = proportion of simulations for which simulated sample A was classified as class i and simulated sample B was classified as class j
1.7
Report
Pr Chii
PrCh11 + PrCh22 + PrCh33 + PrCh44 + PrCh55
Sum of all {PrChij} for which j > i
Sum of all {PrChij} for which j < i
Sum of all {PrChij} for which j = i + 1
Sum of all {PrChij} for which j = i - 1
1.7

## Slide 7: Notes on changes for Model 44
New model 44 only affects prediction. Classification remains unchanged.
We did consider altering the algorithms for errors in map-based environmental variables (used in classification), but decided to leave them unchanged because we may want to add error values in the future (currently, they are unmeasured).

## Slide 8
Prediction
Aim: the prediction of the value of the index expected at the site if it was in the best quality available for that type of site, based on samples collected from best available reference sites.
This is the raw predicted value calculated by RIVPACS prediction, based on environmental variable data input by the user
See separate flow chart for prediction
Prediction
ExpIDXi

## Slide 9
Validation
Checking that the values of environmental input data entered by the user are within suitable ranges
There are three types of validation
Warning limits = min and max values of the environmental variables in RIVPACS ref sites
    When exceeded, RICT provides the user with a warning, but prediction continues
Fail limits = max and min values possible for the environmental variables in NI of GB (or 1% and 100%)
    When exceeded, RICT provides the user with a warning, but prediction does not proceed
Acceptable values = replacement values
    Theoretically there are both min and max values, but currently there are only min values
    When exceeded, RICT substitutes a different value. This is usually to prevent zeros or negative numbers in calculations
1. Data validation
WE1.6 (Section 5)

## Slide 10
Validation for model 44
Warning and fail validation limits need to be determined for new GIS-derived environmental variables
Minimum acceptable values also need to be replaced
Corrected code for determining temperature from lat and long that was incorporated in RICT needs to be incorporated in programme for the new model
GIS-derived map variables need to be renamed so that they are clearly and consistently differentiated from the original variables, e.g. ‘xxxxx_CEH’
1. Data validation
WE1.6 (Section 5)
Validation limits needed for new variables

## Slide 11
Adjustment of expected values to take account of variation in environmental quality of RIVPACS reference sites
Aim: to get standardise raw predictions so that they relate to the same environmental quality (the high/good boundary quality). This is necessary because the best available quality for different types of river varies
Table 9 – adjustment factors and algorithms in WE 4.5
There is one set of adjustment factors for each index
Adjustment factors Aj have only been calculated for a small number of indices, so predictions can only be adjusted for a few indices. Predictions for other indices in RICT cannot be adjusted
Adjust expected
ExpIDXadj,i
Biologists’ assessment values for each end group
Adjustment parameters WHPT Aj
Section WE 4.5
Table 6
(11.1 + 11.1.1, 4.3.7 + 4.7.3.1)

## Slide 12
EQR conversion factor
Aim: to calculate the factor to convert the adjusted predictions that relate to high/good boundary quality to reference values that relate to reference condition, which is somewhere in high status (reference values are the average value of the metric at reference sites in reference condition = high status)
This factor was used to convert the adjusted EQI to EQR in the current RICT
In the new RICT, it is used to convert the adjusted expected to reference value
Each index has a different conversion factor, based on the average value of the index at all RIVPACS Reference Sites divided by the value at RIVPACS reference sites that are in WFD high status (reflected in Biologists’ Assessment values for each reference site).
Conversion factors are in the testing report, below Table 10
EQR conversion factor Ki
Page 20
JMB
(11.5, 4.7.7)

## Slide 13
Convert adjusted expected to reference value
Aim: to convert the predictions from high/good boundary to reference values, which is somewhere in high status (actually the average value of the index at reference sites in high status), by applying the conversion factor
The conversion factor is more logically applied to the adjusted expected value to give an expected reference value. Water Framework Directive expects EQRs to be calculated from reference values and this is what we will follow in the new RICT.
The current RICT and existing documentation applies the conversion to the adjusted EQI to give the EQR.
Ralph Clarke has documented algorithms for the new process in a note produced 4 October.
Convert adjusted expected to reference value
ExpIDXRef = ExpIDXadj,i / Ki
Ralph’s e-mail

## Slide 14
User input of observed index value and bias; calculation of bias adjustment
Aim: input of observed index value, to compare it to prediction of reference and classify its status, based on its deviation from reference
Aim: input of bias to take account of error caused by laboratory analysis, based on results of re-analysis of samples by auditors
RICT classification requires users to input an observed value of an index, based on samples collected in the field.
Users may also input a bias value for Ntaxa, which reflects the impact of analytical error (measured by auditing) on the observed index values
New RICT will calculate multi-season bias adjustment, unlike current RICT (users only have to enter single-season bias)
RICT calculates bias for ASPT from bias for Ntaxa and the observed Ntaxa, using a different formula for Ubiasis
User input observed
ObsIDXi
User input observed sample bias Biasis
Calculate multi-season bias Ubiasis
(7.9, 4.3.11, 6.3.3)

## Slide 15
Simulate uncertainty in observed values
Aim: to take account of errors caused by sampling, based on analysis of sets of replicate samples from the same sites collected by different operators
These simulations take account of sampling error, estimated in replicated sampling studies, including the Biological Assessment Methods Study (BAMS)
They are needed so that statistical confidence of the status classification can be estimated
Ignore WHPT score. In any case, score is derived from ASPT and Ntaxa
Ralph will send revised text for multiple seasons
To combine seasons, average the spring and autumn simulations and classify
Simulated sampling variation in observed
ObsIDXir = ObsIDXi ZNormir * SDObsi
Section 6.3.2
(11.4, -)

## Slide 16
Simulate uncertainty in observed values for Model 44
Decision to leave error eir unchanged.
We considered setting these to zero as there is no field sampling error. However, there is still some imprecision in GIS variables, but has not been measured. We decided to leave algorithm the same so that error values can be replaced if GIS errors are measured or estimated in the future.
Either now or for the future:
We need to confirm the decision to leave error for map-based environmental variables (distance from source, altitude, slope, discharge category) unchanged, because we know GIS is more accurate than manual meaurements by users from maps.
These variables are usually measured now using GIS, even for Model 1, so we may need to consider altering error values in Model 1. Need to check these – perhaps CEH can help.
Simulated uncertainty in reference value ExpIDXRef,ir
= ExpIDXRef,i + eir
Section 6.4 (amended)
(Section 8.5)
Technically, this will differ from Model 1 because most EV data derived from GIS, but we don’t know its true error. Use same error values as Model 1 for safety

## Slide 17
Correct observed values for bias
Aim: to take account of inaccuracy caused by errors in laboratory analysis
Bias is a measure of the impact of laboratory error on the value of observed indices. It is calculated from audits of laboratory performance and is input by users
Variation for bias is also estimated for simulated values of the observed index
Bias adjustment will be mandatory in the new RICT – if bias correction is not wanted, users should set the bias value to zero.
Agreed to use a system default value for Ntaxa (only) if the user does not entere a bias value
Add Ntaxa bias to the sample observed index input – reverting to functionality of RIVPACS III
If no Ntaxa bias values entered into observed index, system should revert to the default value
The numbers referring to different indices (ASPT = 3, Ntaxa = 2, Score = 1) in algorithms in 6.3.3 are unique to that report
Sections highlighted in green in Clarke & Davy-Bowker 2014 replace those in WFD72c Final Report
Ignore 6.3.3.2, because we don’t use unweighted WHPT (nonAb)
Use 6.3.3.3 for WHPT
Don’t incorporate bias values for other indices such as LIFE without speaking to Ralph
Bias corrected observed
ObsIDXirB = ObsIDXir + Ubiasir
Default or user input values for each index – no seasons
Section 6.3.3, 6.3.3.3
(11.1.4, 4.7.3.4)

## Slide 18
Simulate uncertainty in expected
Aim: to take account of error in measurement of environmental variables on the predictions
This takes account of imprecision on the measurement of environmental variables used to predict the reference values
Although 6.4 refers to uncertainty in expected values, the algorithms are the same for reference values
This seems to be covered in the Detailed Functional Specification WFD72cic Section 11.4, even though it’s title is about multiple year classification.
Simulated uncertainty in reference value ExpIDXRef,ir = ExpIDXRef,i + eir
Ralph’s e-mail

## Slide 19
Calculate Environmental Quality Ratio (EQR)
Aim: to express the observed value of the index as an indication of human impact by removing the effect of natural environmental conditions
Status class boundaries for WFD are expressed as EQRs
Simulated EQRs, based on simulated observed and expected values, are needed to estimate probabilities of class
EQR = Bias corrected observed ÷ reference value
(EQRirB = (ObsIDXirB ÷ ExpIDXRef,ir)

## Slide 20
Combine spring and autumn EQRs
Aim: to increase precision of classification and take account of seasonal variations in environmental quality
WFD status must be based on EQRs calculated from spring and autumn samples
Multi-season EQRs are based on the average of EQRs based on spring and autumn samples
Simulated multi-season average EQRr = Av of Sp EQRrSp & Au EQRrAu
Ralph’s e-mail

## Slide 21
Determine the probability of the class being High, Good, Moderate, Poor and Bad status
Aim: to take account of imprecision in monitoring data in the classification
Output the standard deviations and confidence limits (used to be included in RIVPACS III+ but excluded from current RICT). Add information to the user guide about how to use them – e.g. for whiskers when plotting EQRs.
Probability of each class is simply the sum of the simulations resulting in that class.
The Detailed Functional Specification WFD72cic Section 11.1.3, Detailed Functional Specification v3, Section 4.7.3.3 also mentions a face value classification uncorrected for bias. We don’t use that for classification. I’m not sure what it’s used for. I think that this is reported in current RICT classification report as “FVU_CLASS”.
The Detailed Functional Specification WFD72cic Section 11.1.3, Detailed Functional Specification v3, Section 4.7.3.3 also mentions a face value classification corrected for bias. We don’t use that for classification. I’m not sure what it’s used for. I don’t know what it is reported as in the current RICT classification report: possibly AVG_EQI_FVB_CLASS and/or MOST_COMMON_FVB_CLASS.
The Detailed Functional Specification WFD72cic Section 11.4 seems to have a large amount of information about confidence of class for multiple years, but nothing for single year. As multiple year is an addition to single year, that doesn’t seem right and I suspect 11.4 refers to the general situation of dealing with confidence of class.
Identify class using published EQR class (Monte-Carlo simulation)
Prob H
Prob G
Prob M
Prob P
Prob B
Most probable class
Section 6.5
WFD class boundaries

## Slide 22
Determine the worst class indicated by WHPT ASPT and WHPT Ntaxa
Aim: to ensure that the classification reflects ecological impacts caused by any type of environmental pressure
The overall status class for a sample is defined to be the worst of classificaion based on number of taxa and ASPT. This is referred to as the MINTA class (ie MINimum of classes based on number of Taxa and ASPT).
MINTA = Minimum of NTAXA and ASPT
The WFD status of a site or water body is based on the worst class indicated by either WHPY ASPT or WHPT Ntaxa, following the ‘one out all out’ rule.
MINTA
(11.6,4.7.8)

## Slide 23
Determine overall status class based on samples collected in 2- or 3-years
Aim: to take account of temporary differences in quality and improve precision
River Invertebrate status must be assessed every 30-years. Where site are sampled in more than one year I the 3-year monitoring cycle, WFD status can be based on samples collected in more than one year.
Multi-year statu classification takes account of inter-year variation based on observations from River xxxx (Reference)
The current RICT includes this option.
Multi-year
(11.2, 11.3, 11.4, 4.7.4, 4.7.5, 4.7.6)

## Slide 24
Determine overall status class for a water body based on samples collected from more than one site
Aim: to estimate the overall quality of a water body when more than one site is monitored and to improve the precision of the classification
The Environment Agency collects samples from some water bodies from more than one site.
The Environment Agency currently uses VISCOUS software to calculate WFD status for water bodies monitored from more than one site, as ell as sites sampled in more than one year.
Adding new functionality to allow status to be based on data collected from more than one site would streamline the classification process for the Environment Agency.
Because this feature is new, its inclusion is not included in the minimum viable product (MVP) for the new RICT.
Multi-site
Non-MVP

## Slide 25: Classification process in the current RICT
Correct observed for bias
APP_USER_RUN_BIAS.sql
INDICE_CONSTANT.sql
TEMP_BIAS.sql
Adjust expected
END_GROUP_ASSESSMENT.sql
Adjusted EQI = Bias corrected observed ÷ adjusted expected
Convert published class boundaries from EQRs to adjusted EQIs = limit values
Compare adjusted EQI with limit values and report class
TEMP_LIMITS.sql
APP_USER_RUN_LIMITS.sql
Convert adjusted EQI to EQR
Eqr_factor in INDICE_CONSTANT.sql
Published class boundaries
Current RICT
Prediction
Average spring and autumn adjusted EQIs
Probability of class (Monte-Carlo simulation)
Prob H
ProbG
ProbM
ProbP
Prob B
Most probable class
MINTA
Determining class from adjusted EQIs and applying a conversion to EQR conversion afterwards, for reporting
Compare